Copy Cat’s Fuel System

Copy Cat has three fuel tanks.  On her port side she carries two fifty gallon tanks; one dedicated to the engine, and one dedicated to the generator.  On the starboard side, she carries a single 200 gallon tank.

All three tanks can be filled directly; however, the fuel system is designed to take raw  fuel into the starboard tank and use this 200 gallon tank as a supply (filling station) to supply fuel, when needed to the engine or generator tanks.

Fuel is added to either the engine or generator tanks by selecting the desired tank and simply switching on a transfer pump at the main helm dashboard, while observing all three tank levels.

There are not any manifolds, manual valves, or a need to go below to switch valves, and the potential for a valve switching error or air leak is minimized.

When fuel is transferred to either tank it is filtered through a Racor filter and it can be observed, if desired, to be sure that contaminated fuel is not transferred to either the generator or engine tank.

Engine supply

Engine Return

Generator  supply

Generator return

# Text boxes

50 Gal

Eng

Tank

(Port)

50 Gal

Gen

Tank

(Port)

200 Gal

Raw Fuel

Tank

Starboard

Transfer Pump

Transfer Filter

Raw Fuel

Starboard Tank Level

Fuel Transfer Pump

Engine or Generator Tank Level

Selects Engine or Generator

Fuel Pumps This Way